# Repository Information
1. Name
  1. audio_controller_3x2
2. Version
  1. 1.2
3. License
  1. Open-Source Hardware
4. URL
  1. https://github.com/janelia-kicad/audio_controller_3x2
5. Author
  1. Peter Polidoro
6. Email
  1. peterpolidoro@gmail.com
## Description
This board plays audio through a pcb mounted speaker and/or external stereo speakers.
# Images

# Schematic
./schematic/audio_controller_3x2.pdf

# Gerbers
Send gerbers zip file to your favorite PCB manufacturer for fabrication.
./gerbers/audio_controller_3x2_v1.2.zip

# Bill of Materials
## PCB Parts
Item	Reference(s)	Quantity	PartNumber	Vendor	Description
1	C1 C13 C3 C6	4	399-13229-1-ND	digikey	CAP CER 0.1UF 100V X7R 1210
2	C10 C11	2	399-8219-1-ND	digikey	CAP CER 1UF 100V X7R 1210
3	C12 C2 C5 C7	4	478-3591-1-ND	digikey	2.2uF 50V Ceramic Capacitor X7R 1210
4	C4	1	399-15599-1-ND	digikey	0.15uF 100V Ceramic Capacitor X7R 1210
5	C8 C9	2	478-5964-1-ND	digikey	CAP CER 3300PF 2KV X7R 1210
6	J1	1	CP-3523SJCT-ND	digikey	3.50mm Headphone Phone Jack Stereo Connector Solder
7	L1	1	587-1755-1-ND	digikey	FERRITE BEAD 600 OHM 1210 1LN
8	MDB1	2	S1011E-16-ND	digikey	16 Position Header Through Hole Male Pins
9	R1 R2 R3 R4	4	P2.21KAACT-ND	digikey	RES SMD 2.21K OHM 1% 1/2W 1210
10	SP1	1	102-3539-1-ND	digikey	SPEAKER 8OHM 300MW TOP PORT 87DB
11	U1	1	SGTL5000XNAA3R2CT-ND	digikey	Stereo Audio Interface 32-QFN
12	U2	1	AP7313-15SAG-7DICT-ND	digikey	Linear Voltage Regulator IC Positive Fixed 1 Output 1.5V 150mA SOT-23-3
13	U3	1	LM48310SD/NOPBCT-ND	digikey	IC AMP AUDIO PWR 2.6W MONO 10SON

## Supplemental Parts
Item	Quantity	PartNumber	Vendor	Description
1	1	N82E16836121042	newegg	Logitech Z130 5W Speakers

## Vendor Parts Lists
./bom/digikey_parts.csv
./bom/supplemental_newegg_parts.csv
# Supplemental Documentation
## Assembly Instructions
Solder surface mount and through hole components onto the pcb.